## Slide 1
Lauren Magliozzi, M.S. PhD Candidate, CU Boulder
After the Flames | April 15, 2024
Visualizing Watershed Resilience: Lessons on Post-Fire Stream Impacts & Data Communication Techniques from the Marshall Fire

## Slide 2
Lauren Magliozzi PhD Candidate
Chapter 1: Wildland-urban interface wildfire increases metal contributions to stormwater runoff in Paradise, California. (Magliozzi et al., 2024)
Chapter 2: Post-Fire Snowmelt Runoff as a Mechanism for Contaminant Mobilization in a Colorado Wildland-Urban Interface Watershed
Chapter 3: Assessing the ecological impacts of a wildland-urban interface fire on water quality and benthic macroinvertebrate communities in a Colorado watershed.
Ch 1 Environmental Processes & Impacts
(Impacts of 2018 Camp Fire)

## Slide 3: Presentation Overview
Part I: Monitoring impacts of the Marshall Fire on a local watershed
Monitoring project
Results & Conclusions
Part II: Visualizing Data
Considerations
Demonstration & Resources
Brainstorming Session (If Time)

## Slide 4: The Marshall Fire Superior, Louisville, Unincorporated Boulder County
forbes.com
Consumed 6,026 acres in <24 hours on December 30, 2021
Wind gusts up to 106 mph
Destroyed 1,084 structures in the wildland-urban interface fire (WUI)
Est. $1B in destruction, costliest fire in CO history
Est. 10th costliest in USA history

## Slide 5: Coal Creek & the Coal Creek Trail Boulder County, CO
alltrails.com
Coal Creek Trail
14-mile public biking + walking trail along Coal Creek across Boulder County
Connects several open space properties creating a continuous corridor for wildlife & recreation across the county
Coal Creek
Stream & riparian ecosystem in Boulder County that provides habitat for at-risk species:
Rana pipiens
Northern Leopard Frog
CO tier 1 species of greatest conservation need
Preble’s Meadow Jumping Mouse
Zapus hudsonius preblei
Federal list of threatened species
5

## Slide 6: How can wildfires in the WUI impact streams?
Trace & Major Metals
Trace Organics
Nutrients, Sediment
Impermeable Surfaces (e.g., Storm drains)
Streams &
Riparian
Ecosystems
recreation agriculture transportation
6

## Slide 7
1/9/2022, Superior, CO
Hydrologically efficient stormwater collection systems
…channeling runoff into creek

## Slide 8
Basic water quality parameters and nutrients (pH, conductivity, dissolved organic carbon, anions, total suspended solids, and more)
Benthic macroinvertebrate (BMI) Surveys
  Monthly BMI kick-net surveys conducted during baseflow
Water Quality
Methods
Ecosystem Health Methods
Major and trace metals (ICP-MS: Al, Fe, Mn, Zn, Cu, Pb, Ni, Cr, and more; filtered and total fractions)
Grab sampling during monthly baseflow & precipitation events from Jan 2022 – Dec 2023
  Index of biotic integrity used to evaluate pollution tolerance of organisms

## Slide 9: Community Stakeholder Involvement
Project leveraged partnerships with community stakeholders including local land managers, decision makers, and watershed groups
Methods: Hosted monthly stakeholder meetings with updates and results and maintained a public data dashboard
Methods: Organized community outreach events (5+ hosted) and developed an ArcGIS Story Map
Goals: Avoid duplication of effort, target variables & locations of importance to broader community for highest impact
9

## Slide 10
Sampling Locations
Flow
Burned vs. Unburned
Wildland vs. Urban
Chosen to target two sets of variables:
10

## Slide 11
Sampling Locations
Greenbelt Plateau: Upstream unburned wildland site at Greenbelt Plateau Trailhead
11

## Slide 12
Sampling Locations
12
Superior Associates Burned wildland site; Northern Leopard Frog habitat

## Slide 13
Sampling Locations
Hwy 36: Burned urban site, next to large burned structure
abcnews.com
13

## Slide 14
Sampling Locations
14
Dutch Creek Park: Downstream of heavy urban burn

## Slide 15
Sampling Locations
15
Colorado Tech Center (CTC) Open Space: Highly urban area downstream of burn

## Slide 16
Sampling Locations
Mulberry Storm Drain: Collects runoff from burned urban neighborhoods
16

## Slide 17
, increased in urban fire corridor
Selected Results: Total Dissolved Nitrogen in Coal Creek 2022
Flow
Superior Associates
Burned Wildland
Greenbelt
Wildland (unburned)
Hwy 36
Burned Urban
​Dutch Creek Park​
Burned (Fringe) Urban
CTC Open Space
Urban (Downstream)
Low in wildland area
Total Dissolved Nitrogen: Potential urban fire source
Rain events mobilized wildland source of nitrogen
Snowmelt and baseflow conditions reflect this overall trend
and then decreased in urban-only reach of stream
 Total dissolved nitrogen from dominantly burned urban origin
17

## Slide 18
Total Zn: Potential burned wildland & burned urban sources
Baseflow shows both a wildland & burned urban source of total Zn
Rain events show strong burned wildland source
of total Zn
Selected Results: Total Zinc in Coal Creek 2022
Flow
Superior Associates
Burned Wildland
Greenbelt
Wildland (unburned)
Hwy 36
Burned Urban
​Dutch Creek Park​
Burned (Fringe) Urban
CTC Open Space
Urban (Downstream)
Overall

## Slide 19: EPA Aquatic Life Recommended Criteria Limit Exceedances in Coal Creek 2022
# of exceedances
downstream of fire
10
2
14
43
8
39
Chronic: Risk after 4 days of exposure Acute: Risk after 4 hours of exposure
Notes: We also compared our metals data to the EPA aquatic life criteria limit, and so I refer you to these plots which show the number of acute exceedances on the left, and acute limits cause toxicity for organisms that are exposed for an hour or more - and chronic exceedances on the right, which are concentrations that cause toxicity for aquatic life when exceeded for four days or more. I’ve added here the number of exceedances detected downstream of the fire, and you can see that we had exceedances for Cu, Ni, Pb, and Zn, and that the highest number of exceedances in both categories was zinc.
Important to note that the EPA criteria limits do not apply to the Mulberry storm drain but are shown here for broader context

## Slide 20
Zinc Exceedances of EPA Aquatic Life Criteria Acute Limit in Coal Creek in 2022
20x
15x
10x
5x
0x
Acute Exceedance (#-Fold)
Likely snowmelt-mobilized urban fire pulse
Exceedances through the end of 2022
20
Greenbelt Plateau
Highest acute Zn exceedances (>20x, >10x) at burned urban sites
Coincided with highest intensity rain event
Notes: When we look at zinc exceedances in Coal Creek during 2022, we that the creek reached these high concentrations of zinc throughout the year and as late as November. The coordinated debris clean up was implemented from May to August, and the highest acute Zn exceedances of more than 20x the limit, occurred in late August during a high intensity rain event. This shows that contaminants were mobilized into the creek from likely fire sources throughout the year. Using the same approach as the water quality data, we can infer that when exceedances occur in fire-affected areas but not at CTC, we see a likely fire effect.

## Slide 21
Zinc Exceedances of EPA Aquatic Life Criteria Acute Limit in Coal Creek in 2022
20x
15x
10x
5x
0x
Acute Exceedance (#-Fold)
21
Greenbelt Plateau
First major rain event of 2022:
Heavy rain May 4th, and some rain every day from May 2nd to May 5th
April 16, 2022 Highway 36
May 4, 2022 Highway 36
Notes: When we look at zinc exceedances in Coal Creek during 2022, we that the creek reached these high concentrations of zinc throughout the year and as late as November. The coordinated debris clean up was implemented from May to August, and the highest acute Zn exceedances of more than 20x the limit, occurred in late August during a high intensity rain event. This shows that contaminants were mobilized into the creek from likely fire sources throughout the year. Using the same approach as the water quality data, we can infer that when exceedances occur in fire-affected areas but not at CTC, we see a likely fire effect.

## Slide 22: Benthic Macroinvertebrate Count & Index of Biotic Integrity in Early 2022
22
Superior
Burned Wildland
Greenbelt
Unburned
Hwy 36
Burned Urban
CTC
Urban
Superior
Burned Wildland
Greenbelt
Unburned
Hwy 36
Burned Urban
CTC
Urban
May 18, 2022
Two weeks after first rain
April 16, 2022 Two weeks before first major rain
Most Tolerant of Pollution
Least Tolerant of Pollution
Invertebrate Count

## Slide 23: Comparison to Pre-Fire BMI data
2/27
3/12
4/16
5-18
10-30
8-18
6/22
9-30
<1%
36%
13%
30%
0%
17%
13%
0%
Higher percentage of pollution-tolerant organisms post-fire
Hwy 36 (Burned, Urban Site)
July 12, 2019
June 28, 2018
June 22, 2022
Pre-Fire
(Mile High Flood District)
Post-Fire
(This Study)
# of organisms
per meter2:
264
354
1.07
1.20
1.61
*1 Stonefly found at this site
*1 Stonefly found at upstream Hwy 36 site on this date
Shannon diversity:
*No stoneflies ever found post-fire at this site
74
Lower number of organisms per m2 + higher diversity
Site 1
Site 2
July 25, 2022
Presence of plecoptera (stonefly) species indicates likely healthier stream in 2018-2019:
-Stoneflies have no gills on their abdomen, sensitive to reduced DO
-Feed on biolfilm, which may contain metals
-Add photo of plecoptera & some bg maybe, little detail, no gills on their abdomen, more vulnerable to less DO surface area, may take up metals just like an other organism – often shredders, eating bacteria, fungi & algae that may be contamoinated bc they pull metals from the water
Pre-fire presence of Plecoptera (stonefly) species:
- Indicative of a likely healthy stream pre-fire
23

## Slide 24: Preliminary Monitoring Conclusions
Toxic metals & nutrients in Coal Creek likely contributed by the Marshall Fire
  Metals (Cu, Ni, Pb, and Zn) reached levels known to harm aquatic organisms
  Some contaminants (e.g. Zn) were mobilized by rainstorms through late 2022
Impacts on the Coal Creek ecosystem includes community ratios characterized by pollution-tolerant species at burned urban sites and compared to historical data
*Without comprehensive historic data, it is difficult to definitively identify sources of contaminants or recovery status of stream

## Slide 25: Monitoring Project Accomplishments
17 biological assessments
52 water quality sampling dates
255 water quality samples
8,004 benthic invertebrates
>15,000 field and water quality data points collected (and counting)
Importance of long-term monitoring: Sensitive mayfly Leptophlebia cupida has not been observed in the foothills region since the flooding event in 2013! (Found at reference site in 2023)

## Slide 26
Part II. Visualizing Post-Fire Watershed Resiliency
“No Stories Without Numbers, No Numbers Without Stories”
- Dr. Julie Posselt, USC School of Education
AGU Fall Meeting 2023 DEI panel
Notes: Stories connect people to data in an important way!! Allow us to improve communication and understanding

## Slide 27
Enable evidence-based decision making
  Inform policy, prioritize resources, and evaluate recovery efforts
  Promote accountability and trust
Enhance community engagement and empowerment
  Support impacted communities in making safe decisions
  Enable communities to engage in their recovery narrative
Accelerate scientific discovery and understanding
  Facilitate collaboration, reproducibility, and validation
  Lead to new insights, hypotheses, and solutions
Reciprocity:
  Demonstrate transparency, accountability, and public benefit
  Ensure equitable sharing of research benefits
Why make data public?

## Slide 28
Designing an Effective Data Communication Platform
Who is your audience?
Community members (public), or stakeholders with technical knowledge?
How will it be used?
What context will your audience need to understand your data?
                Do you need an FAQ section?
                How will you tell the broader story?
Where will it be hosted and advertised?

## Slide 29
FAQ’s

## Slide 30
Designing an Effective Data Communication Platform
Focus on the most important metrics & keep it simple
Flexibility: Dynamic tools to visualize parameters, sites of interest, and specific timeframes

## Slide 31
Designing an Accessible Data Communication Platform
Colorblind friendly
Alternative text
Conduct usability testing with diverse users
Adhere to web accessibility guidelines and standards Follow the Web Content Accessibility Guidelines (WCAG)
https://www.levelaccess.com/wp-content/uploads/2024/02/ The-Must-Have-WCAG-Checklist.pdf

## Slide 32
Designing an Ethical Data Communication Platform
Consider unintended consequences: Be mindful of how data may inadvertently stigmatize impacted communities
Ethical post-fire data collection
and dissemination:
Always obtain permission
Engage local stakeholders
Involve impacted communities
Respect cultural & ecological sensitivity
Ensure data privacy and security
Environmental Justice

## Slide 33
Tools for Telling a Story: ArcGIS StoryMaps & Google Sites

## Slide 34
Other uses for Data Dashboards: Educational Modules

## Slide 35
Demo: Open-Source Template for Post-Fire Data Dashboard
Used open-source fire monitoring dataset as demonstration Collected by Dr. Charles Rhoades Group (USFS Rocky Mountain Research Station) after the Cameron Peak Fire
Made public by Dr. Matt Ross, CSU (ROSSyndicate, GitHub)
https://github.com/rossyndicate/CPF_reservoir_study_data/tree/v10.18.23

## Slide 36
How to Download from GitHub
https://github.com/LimnologyLauren /Data_Dashboard_Template
Demo: Open-Source Template for Post-Fire Data Dashboard

## Slide 37
Data dashboard template
Meant to be a starting point
Template will continue to be revised as time allows, including accessibility improvements, benthic invertebrate templates, and more
Check back for updates
Suggestions, recommendations, features you want to see? Feel free to reach out!
Final Thoughts
https://github.com/LimnologyLauren /Data_Dashboard_Template

## Slide 38
Sharing data facilitates trust, reciprocity, and collective actions that allow for informed decision making and move science forward
Numbers and narratives are better together to improve engagement and understanding
https://github.com/LimnologyLauren /Data_Dashboard_Template
Final Thoughts

## Slide 39: Acknowledgements
Dr. Julie Korak1, Dr. Cresten Mansfeldt1, Dr. Diane McKnight1,2, Camryn Miller, B.S.1,2 & Lane Allen, M.S.1,2 1CU Boulder, Environmental Engineering Program
2CU Boulder, INSTAAR
PI’s and co-authors:
Funding Partners & Stakeholders:
39

## Slide 40
What are some of the most important considerations for the ethical collection and dissemination of post-fire data?
Brainstorming Session (If Time Allows)
Menti .com Code:
5279
4496
Notes: https://www.mentimeter.com/app/presentation/alq3xc896uripprfk4b8n8qss9dxuffn/6b7bh93m2wuz

## Slide 41
Lauren Magliozzi, M.S. PhD Candidate CU Boulder Environmental Engineering Program and Institute of Arctic & Alpine Research (INSTAAR)
Advisor: Dr. Diane McKnight
Contact Lauren:
Lauren.Magliozzi@colorado.edu
Open to Questions

## Slide 42
Lauren Magliozzi, M.S. PhD Candidate CU Boulder Environmental Engineering Program and Institute of Arctic & Alpine Research (INSTAAR)
Advisor: Dr. Diane McKnight
Contact Lauren:
Lauren.Magliozzi@colorado.edu
Open to Questions

## Slide 43
Supplemental Slides

## Slide 44
Unburned wildland sources
Wildland fire sources
Downstream
urban sources
Urban fire sources
“Background”
Geogenic
Limited highway impacts
Legacy mines
Combusted vegetation
Combusted soil
Combusted infrastructure and vehicles
Road salt/dust
Extensive highway runoff
Potential Origins of Altered Water Chemistry Signatures in Post-Fire WUI Watersheds

## Slide 45
Visualizing Causal Relationships:
RDA
Redundancy
Analysis Used to assess relationships between water quality & explanatory variables
Explanatory variables:
Watershed land use, burn characteristics, TSS, flow, precipitation, mine area, geological background, soil type, etc.
95.93% variance explained
Independent variables: Flow, Percent Urban, # of Destroyed Structures, and TSS
Dependent variables: Total metals, other water quality parameters
(Magliozzi et al., 2024)